## Slide 1
Eugene S. Takle
Department of Agronomy
Department of Geological and Atmospheric Science
Director, Climate Science Program
Iowa State University
Wind Energy Research Group
St Anthony Falls Laboratory
University of Minnesota
16 November 2012
Crop/Wind-energy EXperiment (CWEX):
Results from CWEX10/11 and Vision for the Future

## Slide 2
CWEX Participants
Iowa State University
University of Colorado/
National Renewable Energy Laboratory
National Center for Atmospheric Research
National Laboratory for Agriculture
and the Environment
Ames Laboratory
Anemometry Specialists, Inc
Rajewski, D. A., E. S. Takle, J. K. Lundquist, S. Oncley, J. H. Prueger, T. W. Horst, M. E. Rhodes, R. Pfeiffer, J. L. Hatfield, K. K. Spoth, and R. K. Doorenbos, 2012: CWEX: Crop/Wind-energy Experiment: Observations of surface-layer, boundary-layer and mesoscale interactions with a wind farm. Bull. Amer. Meteor. Soc. (in press)

## Slide 3: Conceptual Model of Turbine-crop Interaction via Mean Wind and Turbulence Fields
__ ___________________________________
Speed recovery
CO2
H2O
Heat
day
night

## Slide 4: CWEX10 Field Experiment
Iowa wind farm ( 200 1.5-MW turbines)
Southern edge of a wind farm
Corn-soybean cropping pattern (measurements made in corn)
26 June – 7 September 2010; turbines off 0700 LST 26 July – 2300 LST 5 Aug 2300
4 Eddy Covariance flux towers
NREL/CU Lidar (J. Lundquist) (28 June-9 July)

## Slide 6
4 flux towers
  maize canopy
  26 June – 7 Sept, 2010
CU/NREL Lidar
  28 June - 9 July 2010

## Slide 9: Case study: 50-min period of wind farm shutdown in nighttime
Dan Rajewski

## Slide 10: Turbines offline: August 27, 2010 2300-0000 LST
Return to reference flow
conditions during the shut
down
80-m wind direction
vector
Station north of two turbine lines has 2-3X ambient TKE and Heat flux before/after OFF period

## Slide 11: Spectral evidence before and during the shutdown period
NLAE 1
NLAE 2
NLAE 3
NLAE 4
NLAE 1
NLAE 2
NLAE 3
NLAE 4
Turbines ON
Turbines OFF
South  North
South  North
ON: Increase in stream-wise momentum variance of: 1.5X downwind of first line of turbines
3.0X downwind of two lines of turbines
OFF: Similar intensity of variance for all flux stations south and north of two turbine lines
V-power spectra

## Slide 12: Spectral evidence before and during the shutdown period
NLAE 1
NLAE 2
NLAE 3
NLAE 1
NLAE 2
NLAE 3
NLAE 4
Turbines ON
Turbines OFF
South  North
South  North
ON: Increase in vertical velocity variance of: 2.0X downwind of first line of turbines
5.0X downwind of two lines of turbines
OFF: Similar intensity of variance for all flux stations south and north of two turbine lines
NLAE 4
W-power spectra

## Slide 13: Spectral evidence before and during the shutdown period
NLAE 1
NLAE 2
NLAE 3
NLAE 1
NLAE 2
NLAE 3
NLAE 4
Turbines ON
Turbines OFF
South  North
South  North
ON: Increase in stream-wise co-variance of 2.0X downwind of first line of turbines
4.0X downwind of two lines of turbines
OFF: Similar intensity of covariance for all flux stations south and north of two turbine lines
NLAE 4
VW-power spectra

## Slide 14: Summary
Turbine wake response is nearly instantaneous to changes in operational characteristics
Significant differences in both flow and microclimate are measurable for surface stations under the influence of two lines of turbines
Spectra of momentum and co-spectra of momentum co-variances demonstrate the asymmetric 3-D wake structure and the translation of this flow pattern to the surface

## Slide 15: CWEX11 Field Campaign
Same location
Measure from June-August
Six measurement stations (instead of 4); four provided by National Center for Atmospheric Research
Two lidars (one upwind, one downwind of turbine line) provided by J. Lundquist, CU
Wind Energy Science, Engineering and Policy Research Experience for Undergraduates (REU) students involved

## Slide 16
Vertically Pointing Lidar
Wind Speed Contours upwind and downwind of B-line of turbines (D = Rotor diameter, ~80 m)
16-17 July 2011
4.5 D South of B-turbines
2.0 D North of B-turbines
Speed difference
Rotor Layer
CU/NREL Lidar research team

## Slide 17
Vertically Pointing Lidar
Vertical profiles of turbulence kinetic energy (TKE)
16-17 July 2011
4.5 D South of B-turbines
2.0 D North of B-turbines
TKE difference
Rotor Layer
CU/NREL/ISU Lidar deployment team

## Slide 18: Analysis by Dan Rajewski
Lidar Data Provided by J.K. Lundquist, M.E. Rhodes, M. Aitken
See also:
M Rhodes: The Effect of Wind Turbine Wakes on Summertime Midwest Wind Profiles
as Observed with Ground Based Doppler LIDAR (NREL seminar available online at
http://wind.nrel.gov/seminars/ )

## Slide 19: Factors influencing turbine wakes
Wind direction
  (centerline vs. periphery effects important to distinguish with downwind distance)
Upwind 80-m wind speed
  (wind speed determines the amount of power generation and wake-turbulence production
Stratification/shear
  (ambient vertical directional shear larger than 30° disorganizes the wake)

## Slide 20: Wake sectors for composites of wind cube and flux station differences (downwind-upwind)
Use the 80 m wind direction
from south wind cube (WC68)
to develop wake windows:
WEST
B12 (WSW)
B23G (between turbines B2 and B3) (SW)
B3 (S)
B34G between turbines B3 and B4 (SSE)
B456h1 (SE)
B456h2 (ESE)
B567h1 (E)
80 m wind direction
from north wind cube (WC49)
to develop wake windows for:
B78 (ENE)
NORTH (NW-NE) (multiple lines of
turbine wakes upstream from this sector)

## Slide 21: Coupled wind cube and surface station differences: vertical velocity (downwind-upwind)
Chart: Vertical velocity difference (m s-1)
| W: n=49 | WSW: n=149 | SW: n=148 | S: n=275 | SSE: n=116 | SE: n=47 | ESE: n=42 | E: n=87 | ENE: n=51 | NW-NE: n=322
WC_120m | -0.01351 | -0.031153 | -0.013074 | 0.069608 | -0.087102 | -0.21437 | -0.16175 | -0.20514 | -0.042146 | -0.16222
WC_80m | 0.00097551 | -0.024252 | -0.048627 | 0.14782 | -0.091791 | -0.13937 | -0.10895 | -0.19642 | -0.092867 | -0.26363
WC_40m | -0.01378 | -0.018364 | -0.020623 | 0.069508 | -0.12566 | -0.034736 | -0.086895 | -0.18543 | -0.1508 | -0.12283
NCAR 2-1 | 0.0050273 | -0.0057366 | -0.014486 | -0.0023283 | -0.0081585 | -0.011093 | -0.0023183 | -0.013717 | -0.0080571 | -0.0030957
NCAR 3-1 | 0.016648 | 0.0052168 | -0.0045551 | -0.0019074 | -0.0050561 | -0.0066128 | 0.0043471 | -0.0030417 | 0.0040898 | 0.0036425
NCAR 4-1 | -0.007831 | -0.012328 | -0.015123 | -0.013849 | -0.024487 | -0.014651 | -0.0027957 | -0.00011575 | -0.0080492 | -0.015063
ISU_2-1 | -0.006188 | 0.00046329 | 0.0044863 | 0.00043833 | 0.0017729 | 0.010205 | 0.001626 | 0.026372 | 0.046567 | 0.031681
(Dw)
Neutral
(Dw)
Stable
Chart: Vertical velocity difference (m s-1)
| WSW: n=73 | SW: n=56 | S: n=242 | SSE: n=184 | SE: n=105 | ESE: n=181 | E: n=140 | ENE: n=124 | NW-NE: n=421
WC_120m | -0.13203 | -0.10521 | -0.014909 | -0.13906 | -0.26234 | -0.28329 | -0.19889 | -0.038002 | -0.048922
WC_80m | -0.08323 | -0.046129 | 0.22071 | -0.11725 | -0.1972 | -0.15766 | -0.15036 | -0.095785 | -0.10836
WC_40m | -0.061718 | -0.059432 | 0.025519 | -0.13505 | -0.099011 | -0.10085 | -0.16654 | -0.14259 | -0.087855
NCAR 2-1 | -0.0073489 | -0.012842 | 0.003297 | -0.0011251 | -0.0062416 | -0.0042312 | -0.013209 | -0.0041412 | 0.003733
NCAR 3-1 | -0.023665 | -0.014201 | -0.0040023 | -0.005199 | -0.017665 | -0.018395 | -0.014726 | -0.016206 | -0.0022569
NCAR 4-1 | -0.0039301 | -0.00036696 | 0.0032782 | -0.0017773 | -0.003027 | -0.0015478 | 0.0036839 | 0.0060687 | 0.013545
ISU_2-1 | -0.0039301 | -0.00036696 | 0.0032782 | -0.0017773 | -0.003027 | -0.0015478 | 0.0036839 | 0.0060687 | 0.013545
Upward velocity
only important in
near-wake centerline
position?
Is uplift an artifact
of the static
pressure field
near the line of
turbines?
Static pressure
effects are weaker
for oblique flow
conditions?
Temperature stratification suppresses vertical motion for isolated wakes?
No significant vertical
motion at the surface

## Slide 22
Vertical velocity (w)
Wind direction (°)
Normalized speed (DU/U0)
Normalized TKE(DTKE/TKE0)
Centerline impacts important for speed, 10-15 degree expansion of other variables
Uplift only in center-line of wake?
Backing wind direction
in wake?

## Slide 23
Vertical velocity (w)
Wind direction (°)
Normalized speed (DU/U0)
Normalized TKE(DTKE/TKE0)
Largest difference seems to peak at an upwind speed near 9 m/s for all variables

## Slide 24: Key Messages
Temperature increases at night in lee of turbines
Temperature decreases during day in lee of the turbines
Wind speed increases in the near lee of the turbines, more for stable flow
Significant wind shear from surface to nacelle particularly under stable flow
Downward CO2 flux is enhanced during day in lee of the turbines
Some evidence for surface layer convergence across a line of turbines

## Slide 25
Surface Pressure Perturbation Produced by a Line of Turbines

## Slide 26
B1
B5
H
L
Grad P
F
Wind Vector
ISU 1
ISU 2

## Slide 27
B1
B5
Wake from B1

## Slide 28
B1
B5
Wake from B1
Wang, H., and E. S. Takle, 1996: On three-dimensionality of shelterbelt structure
and its influences on shelter effects. Bound.-Layer Meteor. 79, 83-105.

## Slide 29
B1
B5
Wake from B1
Sfc
Sfc

## Slide 30
B1
B5
Wake from B1

## Slide 31
Chart: Turbine B1 80-m wind speed, (m/s)
| 3.416166999999997 | 5.391833 | 7.352667 | 7.000167 | 6.985167 | 7.188667 | 7.351666 | 7.461667000000002 | 7.126999999999994 | 7.0035 | 7.037 | 7.48966600000001 | 7.764667 | 7.872333999999999 | 7.575333 | 7.239833000000001 | 7.201 | 6.240334 | 6.811333 | 6.979167000000002 | 6.84 | 6.986333000000001 | 6.802165999999985 | 6.944334 | 6.491167 | 5.018832999999995 | 4.68416599999998 | 3.918 | 4.422832999999994 | 3.338666999999996 | 8.070666000000002 | 8.213000000000001 | 6.835 | 7.180167
STABLE | 28.6 | 104.4 | -6.8 | -6.1 | -3 | -5.6 | -7.4 | -4.5 | -3.3 | -7 | -4.7 | -7.6 | -17.1 | -21.1 | -24.9 | -23.1 | -14.5 | -11.9 | -23.9 | -21.7 | -25.9 | -22.7 | -15.4 | -26.2 | -29.8 | -28.2 | -50.1 | -20.5 | -16.4 | -43.7 | -7.3 | -21.9 | 2.4 | 2.4
NEUTRAL | -2.5 | -4.3 | -8.8 | -8.1 | -7.4 | -4.6 | -6 | -7.9 | -2.4 | 1.5 | -3.5 | -1.4 | 0.1 | -4.8 | -1.6 | -5.5 | -4 | 3.9 | 3.6 | 6.4 | -5.2 | 3.7 | -1.8 | 0.8 | 1.8 | -0.3 | -11 | -2.6 | 3.1 | -2.8 | -7.1 | -6.6 | -5.4 | -4.6 | -4.4 | -9.9 | -4.1 | -7.5 | -6.4 | -8.8 | -7.4 | -6.4 | -17.6 | -4.9 | -3.1 | -1.5 | -6.4 | -8.6 | -12.8 | -2.6
UNSTABLE | -62.3 | -6.4 | 7.8 | -12.8 | 3.2 | 5.7 | -18 | -12
Backing wind at ISU 2
under stable conditions
Southerly Winds, SW at Surface

## Slide 32
B1
B5
Wake from B4

## Slide 33
Chart: Turbine B3 80-m wind speed, (m/s)
Veering wind at ISU 2
under stable conditions
Southerly winds, SE at Surface

## Slide 34
OpenFOAM simulation
Anupam Sharma
Aerospace Engineering Department, Iowa State University
x
x
x
x
x
Turbines
slip surface condition

## Slide 35
OpenFOAM simulation
Anupam Sharma
Aerospace Engineering Department, Iowa State University
p
Veering produced
by pressure gradient
slip surface condition

## Slide 36: Surface Pressure Perturbation Produced by a Line of Turbines
Important factor in driving near-turbine surface flow, especially speed-up in the lee
Some evidence that this pressure field leads to surface convergence within the wind farm
Need to deploy a network of high-accuracy barometers (nanobarometers) to map out the perturbation pressure field both near turbines and across the wind farm

## Slide 37: Measurements Needed
Additional surface flux measurements (middle of wind farm)
Surface pressure field across turbine line
Vertical profiles of horizontal velocity through the turbine layer (H)
Horizontal velocities across the wind farm (convergence?)
Turbulence in and above the turbine layer with the layer above (H-2H); also vertical velocity above the turbine layer
Diurnal changes of u, T, RH, turbulence in H-10H
Low-level jet characteristics

## Slide 38: Analysis Needed
Surface flux anomalies
Wake structure – dependence on stability, speed and direction shear
Coupling of the turbine layer with the layer above (H-2H)
Horizontal convergence in the H layer
Diurnal changes in H-10H
Low-level jet characteristics

## Slide 39: Modeling Needed
Diurnal changes of surface fluxes
Coupling of the turbine layer with the layer above (H-2H)
Horizontal convergence in the H layer
Diurnal changes in H-10H
Low-level jet characteristics
Turbine-turbine interactions (wake characteristics)
Shear and turbulence coupling to blade stresses

## Slide 40: Potential Future Contributions from CWEX
200-turbine utility scale test bed
Flat terrain allows clarity for exploring fundamental interactions of the wind farm with the PBL
Strong diurnal changes in surface layer stratification and resulting shear in speed and direction
Strong Low-Level Jet (similarities to coastal jets as well, horizontal uniformity)
Seasonal land surface change characteristics
Cooperative land owners, multiple field sites
NDA with wind farm operator, access to SCADA data

## Slide 41: Potential Future Contributions from CWEX
Utility scale test bed
Flat terrain allows clarity for exploring fundamental interactions of the wind farm with the PBL
Strong diurnal changes in surface layer stratification and resulting shear in speed and direction
Strong Low-Level Jet (similarities to coastal jets as well, horizontal uniformity)
Seasonal land surface change characteristics
Cooperative land owners, multiple field sites
NDA with wind farm operator, access to SCADA data

## Slide 42
Figure 3. View to the south from Site A.

## Slide 43
Figure 4. View to the north from Site B

## Slide 44: Current Status: Instrumentation
EPSCoR funding for two 120-m instrumented towers
EPSCoR funding for network of surface stations
IGERT funding for nanobarometer network
State of Iowa funding for partnership with a private company for developing a tethered balloon measurement platform (loan of 4 50-m towers, 2 lidars)
Wind farm owner is redeploying 4 sodars to the CWEX site

## Slide 45: Collaborations being Planned
National Laboratory for Agriculture and the Environment will be deploying instruments nearby-but-outside this wind farm in 2013-2015
US Agriculture Research Service plans major field campaign (air-craft, surface, satellite special obs) in 2015
NASA plans major field campaign for satellite soil moisture obs in nearby watershed in 2015

## Slide 46: Summary
CWEX10/11 have demonstrated the feasibility of a major wind farm observing capability in a high-wind resource region of the US.
Educational component in place
Strong interest from
  private sector
  State of Iowa
  Iowa State University
  Federal agencies (NLAE, ARS, NASA, NCAR, NREL)
  University collaborators (CU. UofIowa, UNI)

## Slide 47: For More Information
Eugene S. Takle
gstakle@iastate.edu
http://www.meteor.iastate.edu/faculty/takle/
515-294-9871
Julie K. Lundquist
Julie.Lundquist@colorado.edu
Julie.Lundquist@nrel.gov
http://atoc.colorado.edu/~jlundqui
303/492-8932 (@CU)
303/384-7046 (@NWTC)
Photo courtesy of Lisa H Brasche

## Slide 48: Coupled wind cube and surface station differences: wind direction (upwind-downwind)
(D°)
Neutral
(D°)
Stable
Chart: Wind direction difference (°)
| WSW: n=73 | SW: n=56 | S: n=242 | SSE: n=184 | SE: n=105 | ESE: n=181 | E: n=140 | ENE: n=124 | NW-NE: n=421
WC_120m | 2.5712 | 2.0179 | 7.5826 | 6.768 | 7.6181 | 5.9478 | 7.6686 | 9.4533 | 2.5041
WC_80m | 2.4521 | 2.9411 | 9.1574 | 6.8696 | 9.7724 | 7.1 | 8.5164 | 9.7831 | 1.3016
WC_40m | 1.6781 | 3.4821 | 6.238 | 7.7541 | 10.3238 | 6.2287 | 8.6615 | 10.5256 | 1.023
NCAR_2-1 | -4.9822 | -4.0696 | -2.764 | -0.054639 | 1.1219 | 0.13536 | -0.86929 | 0.35565 | -4.4701
NCAR_3-1 | -4.4274 | -4.2143 | -1.3165 | 0.58557 | 0.64286 | -1.9055 | 0.29571 | 0.15806 | -4.3432
NCAR_4-1 | -4.7918 | -5.1429 | -2.1678 | -0.67577 | -0.8381 | -3.2541 | -1.0779 | -1.8427 | -6.172
Chart: Wind direction difference (°)
| W: n=49 | WSW: n=149 | SW: n=148 | S: n=275 | SSE: n=116 | SE: n=47 | ESE: n=42 | E: n=87 | ENE: n=51 | NW-NE: n=322
WC_120m | 4.4653 | 4.4653 | 3.2819 | 3.8219 | 7.216 | 5.0489 | 6.5447 | 6.4333 | 2.3384 | 2.3542 | 2.4659
WC_80m | 3.2204 | 3.3906 | 5.0784 | 10.5935 | 5.6065 | 9.7702 | 7.069 | 4.9368 | 2.098 | 1.1986
WC_40m | 4.0857 | 3.9503 | 6.8297 | 5.9855 | 6.4011 | 9.5277 | 7.8262 | 4.6743 | 1.5451 | 0.52808
NCAR_2-1 | -5.5776 | -2.8295 | -0.28649 | 0.90545 | 2.0196 | 4.2191 | -2.9214 | -1.9943 | 0.63333 | -6.8671
NCAR_3-1 | -10.0531 | -2.8765 | 0.78986 | 1.9487 | 0.87065 | -1.9298 | -1.8238 | -0.98851 | 2.0333 | -6.6556
NCAR_4-1 | -9.0633 | -4.8738 | 0.96419 | 2.1575 | 1.3022 | -5.0574 | -1.7714 | -2.0874 | 0.52549 | -7.5857
Surface
and upper level
differences
indicate
a strengthening
of CW vertical shear
within the rotor
and an increase
of CCW shear
below the rotor
Wind direction with
the rotor depth
quasi-uniform
for north winds
(far downwind within
leading edge of the wind farm)

## Slide 49
Vertical velocity (w)
Wind direction (°)
Normalized speed (DU/U0)
Normalized TKE(DTKE/TKE0)
Vertical directional shear > 20-25 ° reduces wake influence of all variables
These are for
unstable periods